## Slide 1
An Overview of Txtzyme and SIMPL
* Ward Cunningham’s Txtzyme language
* Ken Boak’s SIMPL language
* How they can be used to command small microcontrollers and other remote devices
* Potential applications of these techniques
John Roberts (jwr39 @ aol.com)
OISF Meeting 9 Dec 2021

## Slide 2
How did I find Txtzyme and SIMPL?
Researching hobbyist FPGA boards
Discovered MyStorm board by Alan Wood (folknology) and Ken Boak (monsonite)
Reading their blogs, Ken had 2013-era postings on SIMPL and Txtzyme
https://sustburbia.blogspot.com/2013/05/txtzyme-minimal-interpreter-and.html
https://sustburbia.blogspot.com/2013/05/more-thoughts-on-txtzyme-and-musical.html
https://sustburbia.blogspot.com/2013/05/simpl-simple-programming-language-based.html
https://sustburbia.blogspot.com/2016/03/simpl-for-beginners-part-1.html

## Slide 3
Ken Boak’s Description of Txtzyme
“Imagine a very simple programming language which could run on any microcontroller with the minimum of on chip resources. A language that could invoke complex instructions and one that could be used to exercise the basic I/O functions of the microcontroller with a simple serial command interface.”
https://sustburbia.blogspot.com/2013/05/txtzyme-minimal-interpreter-and.html

## Slide 4
Original Txtzyme Commands
a-f Select an I/O port
h help - a summary of commands
i input
k a loop counter - which decrements each time around the loop see {}
m millisecond delay
o output
p print the value of variable x followed by carriage return/line feed
s sample an ADC channel
u microsecond delay
x a 16 bit integer variable
{} code between these braces is repeated as a loop
_ _ characters between the underscores are printed to the terminal

## Slide 5
Ken Boak’s SIMPL
“SIMPL stands for Serial Interpreted Minimal Programming Language. It is intended as a common, interactive hardware exercising language that will run on almost any low-end, resource limited, microcontroller.”
Versions for Arduino, Nucleo, LaunchPad, Teensy platforms (by March 2016), more since.
SIMPL written in C, to make it portable.
First port Txtzyme to your microcontroller, then extend it to implement elements of SIMPL.
https://sustburbia.blogspot.com/2016/03/simpl-for-beginners-part-1.html

## Slide 6
LED Flashing Example
SIMPL appears as a series of short ASCII phrases
Make a LED on pin 13 flash 10 times, 100mS on and 1000mS off
13d10{1o100m0o1000m}
13d - select digital pin 13
10{ - set the loop counter to 10 and begin the loop
1o - output 1 (HIGH) to the selected pin
100m - delay for 100 milliseconds
0o - output 0 (LOW) to the pin
1000m delay for 1000 milliseconds
} - loop back to the beginning until the loop counter = 0

## Slide 7
Defining complex commands
If you want to keep this code snippet, you can allocate it to a User Command, normally an uppercase character A-Z. Perhaps use F for flash:
:F13d10{1o100m0o1000m}
Every time you type F the mcu will flash the LED 10 times. The code behind F can be redefined at any time to change the flash behavior
FFFF will execute the code 4 times - flashing the LED 40 times.

## Slide 8
Mostly single-character commands
“SIMPL sets up a minimal serial shell which allows you to control a microcontroller from a few ASCII characters typed from a serial terminal.
Numbers 0-9 are processed as a 16-bit integer and used as numerical input (literals) or as control parameters
Lowercase alpha a-z Usually used to access a predefined routine stored in ROM eg. p is printnumber, u is microsecond delay
Uppercase alpha A-Z Frequently used to define User Commands or parameters, created to meet the requirements of the application
Symbols Used for arithmetic, logic, loop control and program flow purposes.
This convention is suggested as it gives each character a strong mnemonic value and makes the code more readable. However any of the 96 printable ascii characters could be used to initiate any function in code.”

## Slide 9
Implemented with case statement or look-up table
“Each ASCII character acts as an instruction for a command, forcing a jump to a routine that executes the command, before returning to the interpreter to process the next serial character.
The code required to do this is very straightforward and can be implemented as a large switch-case statement or look up table contained within a while loop.
The serial interpreter was first conceived as a means to access and control the Arduino language functions from a serial link, such as digitalWrite, digitalRead, analog, delay, delaymicroseconds, serialPrint etc.
Later arithmetic, logical, looping and program flow operations were added to extend the functionality.”

## Slide 10
Simple Command Loop Interpreter
void textEval(char *buf) {
while ((ch = *buf++)) {
switch (ch) {
case '0': (and other digits)
case 'a': (and other lowercase)
case 'A': (and other uppercase)
case '{': (and other symbols)
} } }
https://github.com/monsonite/SIMPL/blob/master/SIMPL_MSP430F2553.c

## Slide 11
Primitives typically simple, but as complicated as you wish
case 'd': // HEX Dump - dump x bytes starting at address y
hex_dump(x,1024);
print_ok();
break;
case 'f': // File // fill y bytes starting at address x with test data
spi_fill(y,x);
print_ok();
break;
case '$': // print out a number as either a 2 digit or 4 digit Hexadecimal
if(x<=255) {hex_print_2(x); break;}
hex_print_4(x);
break;
case '+':
x = x + y;
y = z;
z = t;
break;

## Slide 12
SIMPL from Feb 2015
a
b
c
d Define a digital port pin
e
f for-next structure
g
h Set an output pin High
i Read an input pin
j
k The loop counter operand
l Set an output pin Low
m A blocking delay in milliseconds
n
o Write to an output pin
p print x to the serial device as an integer number
q
r
s Get an ADC sample
t print the current microsecond count (for timing functions)
u A blocking delay in microseconds
v
w While structure
x The primary data (Accumulator) operand
y The secondary (Address) operand
z Sleep - a non-blocking pause for x seconds while still monitoring UART and I/O

## Slide 13
SIMPL from Feb 2015
Math Group
+ Add x and y and put the result in x
- Subtract x from y and put the result in x
* Multiply x and y and put the result in 32 bit pair [y:x]
/ Divide y by x and put the result in x, and remainder in y
% Calculate y modulo x and put the result in x
space Move the number just entered to y (allows for 2nd variable)
Comparison Group
> If y greater than x, put result in x (equiv to x = y-x)
< If y less than x, put result in x (equiv to x = y-x)
= If y equal to x, put result in x (equiv to x = y-x)
Logical Group
& Bitwise AND of y and x
| Bitwise OR of y and x
^ Bitwise XOR of y and x
~ Bitwise Complement of x
Memory Group
@ Fetch the data into x from the memory address defined by y (PEEK)
! Store the data in x to the memory address defined by y (POKE)
Definition Group
: Start a colon definition
; End a colon definition

## Slide 14
SIMPL from Feb 2015
Block Group
{.......} Loop the code contained within the braces whilst loop variable k is +ve
(.......) Conditionally execute (or skip) the code contained within the round brackets
[,,,,,,,] Create an array of comma separated elements within memory (enumerate and store)
_Print String_ Print the string contained within the underscores
"Store String" Store the string between the quotes in memory
.A. Print the characters assigned to A (list the word A)
'A' Retrieve the string from memory stored at address A
Control and Miscellaneous
? Print out the contents of the program stored in user RAM (LIST)
, A separator between elements stored within memory - store and increment
\ Escape from interpreter - stop all commands
£ Restart interpreter
$ Load x with the ASCII value of next character - do not interpret/execute
# Send a number as a bit pattern to a device, such as port register or shift register
https://sustburbia.blogspot.com/2015/02/simpl-quick-start-guide.html

## Slide 15
Drawing Inspiration from FORTH
SIMPL is like Forth – but simplified!
SIMPL as a universal “Shorthand” allowing us to write code at a fairly low level for a wide variety of microcontrollers – at least for simple applications. I think of it as a debugging toolbox, or Smart Bootloader, that once installed on a microcontroller, grants you the ability to load code into memory, communicate with the mcu at a fairly basic level, execute code and examine the contents of memory or print out results. It also gives the means to exercise the mcu peripherals – such as GPIO, ADC, UART, SPI etc.
SIMPL is essentially a shorthand or shortform of Forth. The two should be designed in such a way that they are interchangeable. SIMPL is just a subset of Forth – simplified!
https://nanode0000.wordpress.com/2017/01/20/simpl-a-small-forth-like-language/
https://nanode0000.wordpress.com/2017/01/21/more-thoughts-simpl-and-eforth/

## Slide 16
Simulator for EDSAC
In September 2017 in Hebden Bridge, the Wuthering Bytes Digital Festival hosted the EDSAC Challenge, in which they attempted to recreate the 1949 Cambridge EDSAC computer as a softcore processor using an FPGA programmed using the IceStorm open source tool chain.
Ken Boak’s contribution to the EDSAC Challenge was to port his SIMPL language toolkit to the 1024 words of EDSAC memory, to see whether it can run on such a minimal architecture, and provide an interactive computing environment.
https://nanode0000.wordpress.com/2017/04/23/an-edsac-simulator-using-simpl/

## Slide 17
SIMPL experiments as cross-compiler for J1 FORTH CPU
SIMPL Operation J1 hex code
” DUP 6081
‘ DROP 6183
$ SWAP 6180
% OVER 6181
+ ADD 6203
& AND 6303
| OR 6403
^ XOR 6503
~ INV 6600
@ FETCH 6C00
! STORE 6123
The cross compiler produces a line of output in response to a single ascii character typed – ^ for XOR
XOR 6503 PC=9 TOP=FFFF DS0=0 DS1=0 DS2=0 DS3=0 RTN=0 MEM20=0 MEM21=6F00 MEM22=0
https://nanode0000.wordpress.com/2017/04/08/exploring-the-j1-instruction-set-and-architecture/

## Slide 18
Applications of SIMPL
Ken Boak already demonstrated:
  Simple language for microcontrollers
  FORTH-like capabilities, very portable
  Toolkit for debugging and manipulating microcontroller
  Simulate CPUs (EDSAC, J1)
Other ideas:
  Command language for controlling IoT devices
  Interpreter for commands sent via network packets to remote devices
  Compact payload for malware or back door

## Slide 19
References
Txtzyme on Federated Wiki http://txtzyme.com/view/welcome-visitors
Txtzyme on Githubhttps://github.com/WardCunningham/Txtzyme
Sustainable Suburbia https://sustburbia.blogspot.com/
Thoughts from the Towpathhttps://nanode0000.wordpress.com/
Ken Boak (monsonite) on GitHub https://github.com/monsonite https://github.com/monsonite/SIMPL

## Slide 20
Questions and Discussion

## Slide 21
Starting Points
Key starting points
https://sustburbia.blogspot.com/2016/03/simpl-for-beginners-part-1.html
https://sustburbia.blogspot.com/2013/05/txtzyme-minimal-interpreter-and.html
https://sustburbia.blogspot.com/2013/05/more-thoughts-on-txtzyme-and-musical.html
https://sustburbia.blogspot.com/2013/05/simpl-simple-programming-language-based.html
Searches for other relevant posts
Search: https://duckduckgo.com/?q=ward+cunningham+txtzyme&ia=web
Search: https://duckduckgo.com/?q=SIMPL+site%3Asustburbia.blogspot.com&ia=web
Search: https://duckduckgo.com/?q=SIMPL+site%3Ananode0000.wordpress.com&ia=web

## Slide 22
Posts on Sustainable Suburbia
Search: https://duckduckgo.com/?q=SIMPL+site%3Asustburbia.blogspot.com&ia=web
https://sustburbia.blogspot.com/2013/05/a-led-chaser-display-using-simpl.html
https://sustburbia.blogspot.com/2013/06/extending-simpl-and-flashing-few-leds.html
https://sustburbia.blogspot.com/2013/06/extensions-to-simpl.html
https://sustburbia.blogspot.com/2013/12/simpl-on-stm32f4xx-discovery-board.html
https://sustburbia.blogspot.com/2013/12/the-elements-of-language.html
https://sustburbia.blogspot.com/2014/05/a-little-more-shifty.html
https://sustburbia.blogspot.com/2014/05/simpl-revisited.html
https://sustburbia.blogspot.com/2015/02/simpl-quick-start-guide.html
https://sustburbia.blogspot.com/2015/09/building-from-ground-up.html
https://sustburbia.blogspot.com/2015/09/extending-simpl.html
https://sustburbia.blogspot.com/2015/09/a-closer-look-at-simpl-interpreter.html
https://sustburbia.blogspot.com/2015/09/how-simpl-can-you-get.html
https://sustburbia.blogspot.com/2015/10/simpl-revisited-again-but-this-time-its.html

## Slide 23
Posts on Sustainable Suburbia
https://sustburbia.blogspot.com/2016/01/a-review-of-tiny-languages-part-1.html
https://sustburbia.blogspot.com/2016/01/a-review-of-tiny-languages-part-2.html
https://sustburbia.blogspot.com/2016/02/a-review-of-tiny-languages-part-3.html
https://sustburbia.blogspot.com/2016/03/simpl-for-beginners-part-1.html
https://sustburbia.blogspot.com/2016/03/simpl-meet-simplex-part-1-putting-it.html
https://sustburbia.blogspot.com/2016/03/simplex-part-2-running-simpl-code-out.html
https://sustburbia.blogspot.com/2016/03/porting-simpl-to-msp430fr4133-launchpad.html

## Slide 24
Posts on nanode0000
Search: https://duckduckgo.com/?q=SIMPL+site%3Ananode0000.wordpress.com&ia=web
https://nanode0000.wordpress.com/2017/01/18/simpl-now-ported-to-msp430-assembly-language/
https://nanode0000.wordpress.com/2017/01/20/simpl-a-small-forth-like-language/
https://nanode0000.wordpress.com/2017/01/21/more-thoughts-simpl-and-eforth/
https://nanode0000.wordpress.com/2017/01/22/making-progress-with-simpl/
https://nanode0000.wordpress.com/2017/04/08/exploring-the-j1-instruction-set-and-architecture/
https://nanode0000.wordpress.com/2017/04/23/an-edsac-simulator-using-simpl/
https://nanode0000.wordpress.com/2017/04/23/using-simpl-as-a-tool-to-bootstrap-unusual-processors/
https://nanode0000.wordpress.com/2017/05/19/more-about-simpl/
https://nanode0000.wordpress.com/2017/05/22/looping-in-simpl/
https://nanode0000.wordpress.com/2017/06/09/simpl-gets-simpler/
https://nanode0000.wordpress.com/2017/08/04/simpl-on-edsac/