## Slide 1: Covert Data Exfiltration - Electromagnetic - Magnetic - Electric - Acoustic - Thermal - Optical - Vibrations - Other
Dr. John W. Carls, CISSP, C|EH

## Slide 2: Electromagnetic
AirHopper (FM Radio)
GSMem (Cellular Frequencies)
USBee (USB emission)
AIR-FI (Wi-Fi Frequencies)

## Slide 3: AirHopper (FM Radio)
Bifurcated malware bridges air-gap using FM signals
Software creates radio emissions from a video display unit (image pattern)
Mobile phone is receiver of radio signals via Digital Signal Processing (DSP) chip
Data exfiltrated at distance of 1-7 meters
Effective bandwidth of 13-60 Bps (Bytes/sec) (104-480 b/sec)

## Slide 4: GSMem (Cellular Frequencies)
Exfiltrate data over cellular frequencies
Software modulates and transmits signals at cellular frequencies by invoking specific memory-related instructions and utilizing the multichannel memory architecture to amplify the transmission
Transmitted signals received and demodulated by a rootkit of a nearby cellular phone
Design issues such as signal generation and reception, data modulation, and transmission detection
Results demonstrate effective transmission distance of 1-5.5 meters
When using a dedicated affordable hardware receiver, the effective distance reached over 30 meters.

## Slide 5: USBee (USB emission)
Use USB connectors implanted with RF transmitters to exfiltrate data
  (e.g., COTTONMOUTH in the leaked NSA ANT catalog)
Requires hardware modification of the USB plug or device, in which a dedicated RF transmitter is embedded
Software utilizes an unmodified USB device as a RF transmitter
Software intentionally generate controlled electromagnetic emissions from the data bus of a USB connector
Emitted RF signals controlled and modulated data
Transmitting data 20 to 80 Bps (bytes per second)

## Slide 6: AIR-FI (Wi-Fi Frequencies)
Attackers can exfiltrate data from air-gapped computers via Wi-Fi signals
Generate signals in the Wi-Fi frequency bands through the memory buses
Nearby Wi-Fi capable devices (e.g., smartphones, laptops, IoT devices) can intercept these signals, decode them, and send them to the attacker over the Internet
Utilize physical layer information exposed by the Wi-Fi chips
Data can be exfiltrated from air-gapped computers to nearby Wi-Fi receivers located a distance of several meters away
https://arxiv.org/abs/2012.06884

## Slide 7: magnetic
MAGNETO (CPU-generated magnetic fields)
ODINI (Faraday shield bypass)

## Slide 8: MAGNETO (CPU-generated magnetic fields)
Data leaked to nearby smartphones via covert magnetic signals
Covert channel works even if kept inside a Faraday shielding case
  Aims to block wireless communication (Wi-Fi, cellular, Bluetooth, etc.)
  Works in airplane mode
Controls magnetic fields emanating by regulating workloads on CPU cores
Smartphone located near computer receives covert signals with its magnetic sensor

## Slide 9: ODINI (Faraday shield bypass)
Air-gapped computers are kept isolated from the Internet because they store and process sensitive information; Might be kept secluded in a Faraday cage
Faraday cage prevents the leakage of electromagnetic signals emanating and provides a high level of isolation
Method is based on the magnetic field generated by the CPU
Low frequency magnetic radiation propagates though the air, penetrating metal shielding such as Faraday cages
Controls low frequency magnetic fields emitted by regulating the load of CPU cores
Data is modulated and transmitted on magnetic emission and received by magnetic receiver

## Slide 10: ODINI (Faraday shield bypass)

## Slide 11: Electric
PowerHammer (power lines)

## Slide 12: PowerHammer (power lines)
Uses power lines to exfiltrate data from air-gapped computers
Control power consumption by regulating CPU utilization
Data is modulated, encoded, and transmitted on current flow fluctuations
Conducted and propagated through the power lines (conducted emission)
Two versions
  Line-level: Taps power lines directly attached to electrical outlet
  Phase-level: Taps power lines at phase-level in service panel
Both versions measures the emission conducted and decodes exfiltrated data
Modulations and encoding schemes with a transmission protocol
Different scenarios, discuss signal-to-noise (SNR), signal processing, and forms of interference
Data can be exfiltrated at bit rates of 1k b/sec for Line-level
  10 bit/sec for Phase-level

## Slide 13: Acoustic
Fansmitter (computer fan noise)
DiskFiltration (hard disk noise)
MOSQUITO (speaker-to-speaker)
POWER-SUPPLAY (Play sound from power supply)
CD-LEAK (sound from CD/DVD drives)

## Slide 14: Fansmitter (computer fan noise)
Utilizes noise emitted from CPU and chassis fans
Regulate internal fans' speed to control acoustic waveform emitted
Modulated and transmitted over audio signals to remote microphone
From a distance of up to eight meters
Rate of 900 b/hour
Method can be used to leak data from different types of IT equipment, embedded systems, and IoT devices that contain fans of various types and sizes

## Slide 15: DiskFiltration (hard disk noise)
Data transmitted via acoustic signals emitted from its hard disk drive (HDD)
Doesn't require the presence of speakers or audio hardware in the air-gapped computer
Generate acoustic emissions at specific audio frequencies by controlling the movements of the HDD's actuator arm and then be picked up by a nearby receiver
Transmitter on a computer and a receiver on a smartphone
Various types of internal and external HDDs in different computer chassis and at various distances
Transmit data to a smartphone at 180 b/minute
Distance of up to two meters (six feet)

## Slide 16: MOSQUITO (speaker-to-speaker)
Computers equipped with passive speakers, headphones, or earphones can exchange data via ultrasonic waves
Microphones are not required
Exploits a specific audio chip feature to reverse connected speakers from output to input devices
  Unobtrusively rendering them microphones
Although reversed speakers not originally designed to perform as microphones
  Still respond well to the near-ultrasonic range (18kHz to 24kHz)
Transmit data nine meters away
Headphones can exchange data three meters apart

## Slide 17: POWER-SUPPLAY (Play sound from power supply)
Exfiltrate data from air-gapped computers through their speakers via sonic and ultrasonic waves
Play sounds and use it as an out-of-band, secondary speaker with limited capabilities
Manipulates the internal switching frequency of the power supply and hence controls the sound waveforms generated from its capacitors and transformers
Technique enables producing audio tones in a frequency band of 0-24khz
Modulated over the acoustic signals and sent to a nearby receiver. Works with:
  PC workstations and servers
  Embedded systems
  IoT devices
Data can be exfiltrated from a distance of 5m at bit rates of 50 b/sec

## Slide 18: CD-LEAK (sound from CD/DVD drives)
“CD-leak: Leaking secrets from audioless air-gapped computers using covert acoustic signals from CD/DVD drives,” in 2020 IEEE 44th Annual Computers, Software, and Applications Conference (COMPSAC). IEEE, 2020, pp. 808–816.

## Slide 19: Thermal
BitWhisper (CPU generated heat)
HOTSPOT (CPU generated heat received by smartphone)

## Slide 20: BitWhisper (CPU generated heat)
Using heat emissions and thermal sensors
Unique in two respects:
  Supports bidirectional communication
  Requires no additional dedicated peripheral hardware
Experiments included different layouts, varying distances, several sensor types, and CPU configurations (e.g., Virtual Machines)
Heat Generated by CPU/GPU Stress Test
Exchange data in close proximity (at distance of 1-40cm)
Effective rate of 1-8 bits per hour
  Makes it possible to infiltrate brief commands and exfiltrate small amount of data

## Slide 21: HOTSPOT (CPU generated heat received by smartphone)
“Hotspot: Crossing the air-gap between isolated PCs and nearby smartphones using temperature,” in 2019 European Intelligence and Security Informatics Conference (EISIC). IEEE, 2019, pp. 94–100.

## Slide 22: Optical
LED-it-GO (Hard Drive LED)
Keyboard LEDs
xLED (Router LEDs)
aIR-Jumper (Security Cameras and Infrared)

## Slide 23: LED-it-GO (Hard Drive LED)
Utilizes the hard disk drive (HDD) activity LED rapidly (up to 5800 blinks per second)
Received remotely by different kinds of cameras and light sensors
  Demonstration video: https://www.youtube.com/watch?v=4vIu8ld68fc
Unique because HDD activity LED routinely flickers frequently, and therefore not suspicious of changes in activity
Examined different colored HDD LEDs (red, blue, and white)
Tested different receivers: remote cameras, ‘extreme’ cameras, security cameras, smartphone cameras, drone cameras, and optical sensors
Data leaked at 120 b/s (bits per second) when video camera is used, 4k b/s when light sensor is used (Speed is 10 times faster)
Computer LEDs detected up to 30 m

## Slide 24: CTRL-ALT-LED: Keyboard LEDs
Uses Keyboard LEDs to send data optically
Uses Caps-Lock, Num-Lock, and Scroll-Lock to encode information and exfiltrate data
Presents transmission protocol and modulation schemes
Test various receivers, light sensors, remote cameras, 'extreme' cameras, security cameras, and smartphone cameras
Data can be leaked via the keyboard LEDs at a bit rate of 3k b/sec per LED
  120 b/sec if smartphone used
CTRL-ALT-LED: Leaking Data from Air-Gapped Computers Via Keyboard LEDs https://ieeexplore.ieee.org/document/8754078

## Slide 25: xLED (Router LEDs)
Covertly leak data via status LEDs in switches and routers
Controlling status LEDs to carry data
Data encoded and modulated over blinking LEDs
Signals recorded by remote cameras and optical sensors
Evaluated a few routers and different types of LEDs
Tested various receivers including: remote cameras, security cameras, smartphone cameras, and optical sensors
Data leaked via LEDs at 10 b/sec to more than 1Kbit/sec per LED

## Slide 26: aIR-Jumper (Security Cameras and Ir)
IR is invisible to humans, but cameras are optically sensitive
Use of surveillance cameras and IR to establish bi-directional covert communication between the internal networks of organizations and remote attackers
Two scenarios: Exfiltration (leaking data out of the network) and Infiltration (sending data into the network)
  Exfiltration. Surveillance and security cameras are equipped with IR LEDs, which are used for night vision
    Access surveillance cameras across network and controls IR illumination
    Sensitive data such as PIN codes, passwords, and encryption keys are modulated, encoded, and transmitted over IR
  Infiltration. In an infiltration scenario, an attacker standing in a public area (e.g., in the street) uses IR LEDs to transmit hidden signals to the surveillance camera(s). Binary data such as command and control (C&C) and beacon messages are encoded on top of the IR signals
Exfiltration and infiltration combined to establish bidirectional, 'air-gap' communication between the compromised network and the attacker
Data exfiltrated at 20 b/sec per surveillance camera to distance tens of meters away
Data infiltrated at 100 b/sec per surveillance camera from distance hundreds to kilometers away

## Slide 27: Vibrations
AiR-ViBeR (Computer Fan vibrations)

## Slide 28: AiR-ViBeR (Computer Fan vibrations)
Vibrational (seismic) covert channel
Computers vibrate at a frequency correlated to the rotation speed of internal fans
Covert vibrations sensed by nearby smartphones via sensitive accelerometers
  Encodes information, modulates over a low frequency vibrational carrier
  Decoded by application on smartphone placed on the same surface
  Up to 160 cm
Data can be exfiltrated from air-gapped computer via vibrations

## Slide 29: Other - HVACKer: Bridging the Air-Gap by Attacking the Air Conditioning System
Modern corporations physically separate their sensitive computational infrastructure from public or other accessible networks in order to prevent cyber-attacks
Attackers still manage to infect these networks, either by means of:
  An insider
  By infiltrating the supply chain
Air-gapped network receives communications over a covert thermal channel
Use a compromised air-conditioning system (connected to the internet) to send commands

## Slide 30: Other – Oops!... I think I scanned Malware
Proof-of-Concept illustrating feasibility of creating a covert channel between a C&C server and an organization's scanner
Uses light sensitivity of a flatbed scanner
Various experimental setups using:
  Laser connected to a stand
  Laser carried by a drone
  Hijacked smart bulb
Infiltrate data using different light sources
Distance of 900 m

## Slide 31: Summary